## Slide 1: Measuring Instruments
Ruler
1 A ruler is used to measure lengths from a few cm up to 1 m. A metre rule has an accuracy of 0.1 cm (i.e. 1 mm).

## Slide 2: Measuring Instruments
Ruler
2 Precautions to be taken when using a ruler:
(a) Ensure that the object is in contact with the ruler to avoid inaccurate readings.
(b) Avoid parallax errors.

## Slide 3: Measuring Instruments
Ruler
Parallax errors in measurement arise as a result of taking a reading, with the eye of the observer in the wrong position with respect to the scale of the ruler. Figure 1.7 shows the correct position of the eye when reading the scale.
Error = 0.1 cm
Error = 0.1 cm

## Slide 4: Measuring Instruments
Ruler
(c) Avoid zero and end errors.
The ends of a ruler, which may be worn out, are a source of errors in measurement. Thus it is advisable to use the division mark `1' of the scale as the zero point when taking a measurement.

## Slide 5: Measuring Instruments
Ruler
(c) Length of the block, l =3.2cm-1.0cm = 2.2 cm

## Slide 6: Measuring Instruments
1 Lengths smaller than 1 mm can be measured with the help of an instrument called a vernier caliper.
Vernier Caliper

## Slide 7: Measuring Instruments
Vernier Caliper
2 A vernier caliper is used to measure an object with dimensions up to 12 cm with an accuracy of 0.01 cm.

## Slide 8: Measuring Instruments
Vernier Caliper
3 There are two pairs of jaws, one is designed to measure linear dimensions and external diameters while the other is to measure internal diameters.

## Slide 9: Measuring Instruments
Vernier Caliper
4. To measure with a vernier caliper, slide the vernier scale along the main scale until the object is held firmly between the jaws of the caliper. The subsequent steps are as follows.

## Slide 10: Measuring Instruments
Vernier Caliper
(a)The reading on the main scale is determined with reference to the `0' mark on the vernier scale. The reading to be taken on the main scale is the mark preceding the Figure 1.10 shows that the '0' mark on the vernier scale lies between 3.2 cm and 3.3 cm. The reading to be taken on the main scale is 3.2 cm (the `0' mark on the vernier scale acts as a pointer).
1

## Slide 11: Measuring Instruments
Vernier Caliper
(b) The reading to be taken on the vernier scale is indicated by the mark on the vernier scale which is exactly in line or coincides with any main scale division line. Figure 1.10 shows that the fourth mark on the vernier scale is exactly in line with a mark on the main scale. Thus the second decimal reading of the measurement is:
Vernier scale reading = 4 x 0.01 cm
= 0.04 cm
2

## Slide 12: Measuring Instruments
Vernier Caliper
(c) The reading of the vernier caliper is the result of the addition of the reading on the main scale to the reading on the vernier scale.
3.2
0.04

## Slide 13: Measuring Instruments
Vernier Caliper
(c) The reading of the vernier caliper is the result of the addition of the reading on the main scale to the reading on the vernier scale.
Caliper reading = Main scale Reading + Vernier scale reading
Thus the reading of the vernier caliper in Figure 1.10 is
= 3.2 + 0.04 = 3.24 cm
3.2
0.04

## Slide 14: Measuring Instruments
Vernier Caliper
5. A vernier caliper has a zero error if the `0' mark on the main scale is not in line with the '0' mark on the vernier scale when the jaws of the caliper are fully closed

## Slide 15: Measuring Instruments
Vernier Caliper
(a) Positive zero error
Zero error = +0.04 cm.

## Slide 16: Measuring Instruments
0.72 cm
0.70 cm
0.02cm

## Slide 17: Measuring Instruments
Vernier Caliper
(b) Negative zero error
Zero error = -0.02 cm.

## Slide 18
What is the result of measuring ?

## Slide 19
What does it mean ?

## Slide 20
6 mm

## Slide 21
What does it mean ?

## Slide 22
( 2 x 0.1 ) mm

## Slide 23
6 mm
( 2 x 0.1 ) mm
The result of measuring is ( 6 mm + 0.2 mm ) = 6.2 mm

## Slide 24
What is the result of measuring ?

## Slide 25
The result of measuring is :
( 3 mm + ( 7 x 0.1 ) mm ) = 3.7 mm

## Slide 26: Measuring Instruments
Micrometer Screw Gauge
1 A micrometer screw gauge is used to measure small lengths ranging between 0.10 mm and 25.00 mm.

## Slide 27: Measuring Instruments
Micrometer Screw Gauge
2 This instrument can be used to measure diameters of wires and thicknesses of steel plates to an accuracy of 0.01 mm.

## Slide 28: Measuring Instruments
Micrometer Screw Gauge
3 The micrometer scale comprises a main scale marked on the sleeve and a scale marked on the thimble called the thimble scale.

## Slide 29: Measuring Instruments
Micrometer Screw Gauge
4 The difference between one division on the upper scale and one division on the lower scale is 0.5 mm.

## Slide 30: Measuring Instruments
Micrometer Screw Gauge
5 The thimble scale is subdivided into 50 equal divisions. When the thimble is rotated through one complete turn, i.e. 360, the gap between the anvil and the spindle increases by 0.50 mm.

## Slide 31: Measuring Instruments
Micrometer Screw Gauge
6 This means that one division on the thimble scale is = 0.01 mm.

## Slide 32: Measuring Instruments
Micrometer Screw Gauge
7 When taking a reading, the thimble is turned until the object is gripped very gently between the anvil and the spindle.

## Slide 33: Measuring Instruments
Micrometer Screw Gauge
8 The ratchet knob is then turned until a `click' sound is heard.

## Slide 34: Measuring Instruments
Micrometer Screw Gauge
9 The ratchet knob is used to prevent the user from exerting undue pressure.

## Slide 35: Measuring Instruments
Micrometer Screw Gauge
10 The grip on the object must not be excessive as this will affect the accuracy of the reading.

## Slide 36: Measuring Instruments
Micrometer Screw Gauge
11 Readings on the micrometer are taken as follows.
(a) The last graduation showing on the main scale indicates position between 2.0 mm and 2.5 mm. Thus the reading on the main scale is read as 2.0 mm.

## Slide 37: Measuring Instruments
Micrometer Screw Gauge
11 Readings on the micrometer are taken as follows.
(b) The reading of the micrometer screw gauge is the sun of the main scale reading and the thimble scale reading which is:
2.0 + 0.22 =2.22 mm

## Slide 38: Measuring Instruments
Micrometer Screw Gauge
11 Readings on the micrometer are taken as follows.
(b) The reading on the thimble scale is the point where the horizontal reference line of the main scale is in line with the graduation mark on the thimble scale Figure 1.15(b) shows this to be the 22nd mark on the thimble scale, thus giving a reading of 22 x 0.01 mm = 0.22 mm.

## Slide 39: Measuring Instruments
Micrometer Screw Gauge
12 Readings on the micrometer are taken as follows.
(a) Positive zero error
In Figure 1.16, the horizontal reference line in the main scale is in line with the 4th division mark, on the positive side of the `0' mark, on the thimble scale. The error of +0.04 mm must be subtracted from all readings taken.
Zero error = +0.04 mm

## Slide 40: Measuring Instruments
Micrometer Screw Gauge
13(b) Negative zero error
In Figure 1.17, the horizontal reference line on the main scale is in line with the 3rd division mark, below the `0' mark of the thimble scale.
Zero error = -0.03 mm