## Slide 1: TURNING EFFECT OF FORCES

## Slide 2: Specification
TURNING EFFECT
know and use the relationship:
moment = force × perpendicular distance from the pivot
know that the weight of a body acts through its centre of gravity
know and use the principle of moments for a simple system of parallel forces acting in one plane
understand that the upward forces on a light beam, supported at its ends, vary with the position of a heavy object placed on the beam

## Slide 3: The moment of a force
Also known as the turning effect of a force.
The moment of a force about any point is defined as:
moment = force x perpendicular distance from the pivot
moment = F x d
Unit: newton-metre (Nm)
Moments can be either CLOCKWISE or ANTICLOCKWISE
Force F exerting an ANTICLOCKWISE moment through the spanner on the nut

## Slide 4: Question
Calculate the moment exerted with the claw hammer if the person exerts a force of 80N and distance d equals 25cm.
moment = F x d
= 80N x 25cm
= 80N x 0.25m
= 20 Nm CLOCKWISE

## Slide 5: Complete:
Force (N) | Distance | Moment (Nm)
40 | 3 m | 
200 |  | 1000
 | 4 m | 200
3000 | 20 cm | 
Answers

## Slide 6: Complete:
Force (N) | Distance | Moment (Nm)
40 | 3 m | 120
200 | 5 m | 1000
50 | 4 m | 200
3000 | 20 cm | 600
Answers
120
5 m
50
600

## Slide 7: Question
Choose appropriate words to fill in the gaps below:
The ‘moment of a force’ is another name for the ‘________ effect of force’.
The moment of a force is equal to the ________ multiplied by the perpendicular _________ between the line of ________ of the force and the turning point.
Turning effect is measured in _________ metres.
__________ can be either clockwise or anticlockwise.
moments
turning
action
newton
distance
WORD SELECTION:
force

## Slide 8: Question
Choose appropriate words to fill in the gaps below:
The ‘moment of a force’ is another name for the ‘________ effect of force’.
The moment of a force is equal to the ________ multiplied by the perpendicular _________ between the line of ________ of the force and the turning point.
Turning effect is measured in _________ metres.
__________ can be either clockwise or anticlockwise.
moments
turning
action
newton
distance
WORD SELECTION:
force
moments
turning
action
newton
distance
force

## Slide 9: Centre of gravity
centres of gravity of regular shapes
The centre of gravity of a body is that point at which the weight of the body acts.
The centre of gravity of a symmetrical body is along the axis of symmetry.
Centre of gravity is also sometimes called centre of mass.

## Slide 10
If suspended, a body will come to rest with its centre of gravity directly below the point of suspension.
Centre of gravity

## Slide 11: Finding the centre of gravity of a card
Centre of gravity
Pierce the card in at least two places.
Suspend the card from one of these holes.
Hang a plumbline from the point of suspension.
Using the plumbline as a reference draw a vertical line on the card.
Repeat for the other hole(s).
The centre of gravity is where the lines cross on the card.

## Slide 12: Stability
A body is stable as long as its centre of gravity remains vertically above its base.
If this is not the case, the body will topple.
stable
Centre of gravity
unstable - toppling
Centre of gravity
balanced
Centre of gravity

## Slide 13: Question
What factors make a modern racing car as stable as possible?
1. A wide wheel base.
2. A low centre of gravity.

## Slide 14: The principle of moments
When an object is not turning (e.g. balanced):
The total clockwise moment equals the total anticlockwise moment
If the ruler above is balanced:
clockwise moment = anticlockwise moment
W2 x d2 = W1 x d1

## Slide 15: Question 1
On a see-saw Mary, weight 600N balances John, weight 200N when she sits 1.5m away from the pivot. How far from the pivot is John?

## Slide 16: Question 1
On a see-saw Mary, weight 600N balances John, weight 200N when she sits 1.5m away from the pivot. How far from the pivot is John?
Applying the principle of moments:
Mary’s weight x distance = John’s weight x distance
600N x 1.5m = 200N x distance
900 = 200 x distance
900 ÷ 200 = distance
John is 4.5m from the pivot

## Slide 17: Question 2
Calculate the weight of the beam, W0 if it is balanced when:
W1 = 6N;
d1 = 12 cm;
d0 = 36 cm.

## Slide 18: Question 2
Calculate the weight of the beam, W0 if it is balanced when:
W1 = 6N;
d1 = 12 cm;
d0 = 36 cm.
Applying the principle of moments:
W1 x d1 = W0 x d0
6N x 12 cm = W0 x 36 cm
W0 = 72 / 36
W0 the weight of the beam = 2N

## Slide 19
Complete for a balanced ruler:
W1 | d1 | W2 | d2
5 N | 20 cm | 10 N | 
4 N | 15 cm |  | 10 cm
6 N |  | 2 N | 36 cm
 | 25 cm | 2 N | 100 cm

## Slide 20
Complete for a balanced ruler:
W1 | d1 | W2 | d2
5 N | 20 cm | 10 N | 10 cm
4 N | 15 cm | 6 N | 10 cm
6 N | 12 cm | 2 N | 36 cm
8 N | 25 cm | 2 N | 100 cm
10 cm
6 N
12 cm
8 N

## Slide 21: Forces on a beam or bridge
When the lorry is at the centre of the bridge its weight will be supported equally by the two columns A and B.
Column A
Column B
lorry weight = 24 000N
12 000N
12 000N

## Slide 22
When the lorry was over columns A all of its weight would have been supported by this column
Column A
Column B
lorry weight = 24 000N
24 000N

## Slide 23
When the lorry is ¾ the way across the bridge column B will bear ¾ of its weight. Column A bears the remaining ¼.
Column A
Column B
lorry weight = 24 000N
6 000N
18 000N

## Slide 24
What are the column forces when the lorry is one third the way across the bridge?
Column A
Column B
lorry weight = 24 000N
16 000N
8 000N

## Slide 25: Question
Choose appropriate words to fill in the gaps below:
The turning effect of a ________ is also called the ________ of a force. Moment is measured in _________ metres.
If a body is balanced the total clockwise moment is _______ to the total ____________ moment.
A body will be _______ if its centre of gravity lies vertically above the _______ of the body. A tractor has a large wheel base to reduce the possibility of it __________.
newton
moment
equal
toppling
anticlockwise
stable
WORD SELECTION:
base
force

## Slide 26: Question
Choose appropriate words to fill in the gaps below:
The turning effect of a ________ is also called the ________ of a force. Moment is measured in _________ metres.
If a body is balanced the total clockwise moment is _______ to the total ____________ moment.
A body will be _______ if its centre of gravity lies vertically above the _______ of the body. A tractor has a large wheel base to reduce the possibility of it __________.
newton
moment
equal
toppling
anticlockwise
stable
WORD SELECTION:
base
force
newton
moment
equal
toppling
anticlockwise
stable
base
force