## Slide 1: HABER PROCESS

## Slide 2: What is ammonia?
It is made industrially by reacting nitrogen with hydrogen in the Haber process. It is a reversible reaction, so it never goes to completion.
hydrogen
nitrogen
+
ammonia
N2 (g)
3H2 (g)
2NH3 (g)
+
Ammonia is an important compound in the manufacture of fertilizer and other chemicals such as cleaning fluids and floor waxes.
Why is this a problem for companies making ammonia?
Notes: Photo credit: © 2007 Jupiterimages Corporation

## Slide 3: The Haber process
Notes: Teacher notes
This five-stage animation illustrates how ammonia is made in the Haber process.

## Slide 4: A flow diagram
Purifier
and
drier
N2
H2
Compression
Chamber
(200 atm)
Clean
Dry
N2 &
H2
Heat
exchanger
Catalytic
chamber
Condenser
Liquid NH3 to storage
Unreacted N2 , H2

## Slide 5: What is yield?
The amount of product made in a reaction is called the yield and is usually expressed as a percentage.
ammonia yield (%)
pressure (atm)
The yield of ammonia produced by the Haber process depends on the temperature and pressure of the reaction.
Notes: Teacher notes
See the ‘Quantitative Chemistry’ presentations for more information on yields.

## Slide 6: What is the Haber compromise?
In practice, though, these conditions are not used. Why?
The highest yield of ammonia is theoretically produced by using a low temperature and a high pressure.
A compromise is reached to make an acceptable yield in a reasonable timeframe while keeping costs down.
Lowering the temperature slows down the rate of reaction. This means it takes longer for ammonia to be produced.
Increasing the pressure means stronger, more expensive equipment is needed. This increases the cost of producing the ammonia.
Notes: Photo credit: Davis Hay Jones / Science Photo Library

## Slide 7: Temperature, pressure and yield
Notes: Teacher notes
This activity could be used as a plenary or revision exercise on the effects of temperature and pressure on the Haber process.

## Slide 8
N2(g) + 3H2(g) 2NH3(g) : DH = - 92 kJ mol-1
Conditions Pressure 20000 kPa (200 atmospheres)
Temperature 380-450°C
Catalyst iron
HABER PROCESS

## Slide 9
N2(g) + 3H2(g) 2NH3(g) : DH = - 92 kJ mol-1
Conditions Pressure 20000 kPa (200 atmospheres)
Temperature 380-450°C
Catalyst iron
Equilibrium theory favours
low temperature exothermic reaction - higher yield at lower temperature
high pressure decrease in number of gaseous molecules
HABER PROCESS

## Slide 10
N2(g) + 3H2(g) 2NH3(g) : DH = - 92 kJ mol-1
Conditions Pressure 20000 kPa (200 atmospheres)
Temperature 380-450°C
Catalyst iron
Equilibrium theory favours
low temperature exothermic reaction - higher yield at lower temperature
high pressure decrease in number of gaseous molecules
Kinetic theory favours
high temperature greater average energy + more frequent collisions
high pressure more frequent collisions for gaseous molecules
catalyst lower activation energy
HABER PROCESS

## Slide 11
N2(g) + 3H2(g) 2NH3(g) : DH = - 92 kJ mol-1
Conditions Pressure 20000 kPa (200 atmospheres)
Temperature 380-450°C
Catalyst iron
Equilibrium theory favours
low temperature exothermic reaction - higher yield at lower temperature
high pressure decrease in number of gaseous molecules
Kinetic theory favours
high temperature greater average energy + more frequent collisions
high pressure more frequent collisions for gaseous molecules
catalyst lower activation energy
Compromise conditions
Which is better? A low yield in a shorter time or
a high yield over a longer period.
The conditions used are a compromise with the catalyst
enabling the rate to be kept up, even at a lower temperature.
HABER PROCESS

## Slide 12
IMPORTANT USES OF AMMONIA AND ITS COMPOUNDS
MAKING
FERTILISERS 80% of the ammonia produced goes to make fertilisers such as
ammonium nitrate (NITRAM) and ammonium sulphate
NH3 + HNO3 ——> NH4NO3
2NH3 + H2SO4 ——> (NH4)2SO4
MAKING
NITRIC ACID ammonia can be oxidised to nitric acid
nitric acid is used to manufacture... fertilisers (ammonium nitrate)
explosives (TNT)
polyamide polymers (NYLON)
HABER PROCESS

## Slide 13: The Haber compromise
To produce a high yield of ammonia, but with a fast rate of reaction and without the need for overly expensive equipment, the Haber process is carried out at 450 °C and 200 atmospheres.
The most important factor in deciding what conditions to use is therefore not yield, but total cost.
raw materials
equipment
energy
wages
What costs are involved in the industrial production of ammonia?
Notes: Photo credit: © 2007 Jupiterimages Corporation

## Slide 14: Maximizing productivity
What else can be done to maximise productivity in the manufacture of ammonia?
An iron catalyst is used to increase the rate of reaction. It speeds up both the forward and backward reaction, so the position of equilibrium is not affected.
The ammonia is cooled, liquefied and then removed as it is produced. This causes the equilibrium to shift to the right to produce more ammonia.
Unreacted nitrogen and hydrogen are recycled and given another chance to react.

## Slide 15: Stages of the Haber process
Notes: Teacher notes
This ordering activity could be used as a plenary or revision exercise on the stages in the Haber process. Mini-whiteboards could be used to make this a whole-class exercise.

## Slide 16: Glossary
closed system – A system in which reactants and products cannot be added or removed once the reaction has begun.
dynamic – An equilibrium in which the forward and backward reactions take place at the same rate, so no overall change takes place.
Haber process – The industrial-scale process for making ammonia from nitrogen and hydrogen.
irreversible – A reaction that is impossible or very difficult to reverse.
reversible – A reaction in which the product(s) can be turned back into the reactants.
yield – The amount of product obtained from a reaction,
usually expressed as a percentage.