## Slide 1: Capacitor
An element that stores charge when a voltage is applied
Q = CV (definition)
C is the capacitance
  Unit is farad or C/V or C2/Nm or C2/J
Capacitance is a function of geometry and material

## Slide 2
Capacitors
A capacitor can be of any two conductors isolated
Parallel plates are just a easy way to think of the problem
General method to calculate
a) Assume a charge on the conductors
b) Calculate the voltage difference due to the charge
` c) Ratio Q/V is the capacitance

## Slide 3: Capacitor as a circuit element
Typical value of a capacitor
    A few mF
Adding capacitors in series and parallel
Calculating charge and voltage on a capacitor

## Slide 4
(a) Two capacitors in parallel, (b) the equivalent circuit.
Ceq = C1 + C2
Parallel Capacitors
Across C1 and C2
Voltage same
Charge splits

## Slide 5
(a) Two capacitors in series (b) the equivalent capacitor.
1 / Ceq = 1 / C1 + 1 / C2
Series Capacitors
Across C1 and C2
Charge same
Voltage splits

## Slide 6: Capacitor practice
A
B
C1
C2
C1 = 4 mF, C2 = 2 mF
What is total capacitance from A to B

## Slide 7: Capacitor practice
C1 = 4 mF, C2 = 2 mF, C3 = 2 mF
What is total capacitance from A to B
A
B
C1
C2
C3
Notes: ¼ + ½ + ½ = 5/4 so C = 4/5 =.8 mF

## Slide 8: Capacitor practice
C1 = 4 mF, C2 = 4 mF, C3 = 2 mF, C4 = 2 mF
What is total capacitance from A to B
A
B
C1
C2
C3
C4
Notes: C1 + C2 = 2.0mF, C3 + C12 = 4mF, C4 + C123 = 4/3 mF

## Slide 9
Typical Capacitance Problem: 1
Find the equivalent capacitance
What is the voltage across capacitor C2
C1
C2
C3
A
B
C1 = 4.0 mF, C2 = C3 = 1.0mF, VAB = 3.0 V

## Slide 10
Typical Capacitance Problem: 2
Given 9V across the elements what is the charge on C1
C1 = C2 = 1.5 nF, C3 = C4 = 3.0 nF, VAB = 9.0 V
C1
C3
A
B
C4
C3

## Slide 11: Energy Storage in Capacitors
When we charge a capacitor we have stored energy in the capacitor
    U = Q2/2C
Using C=Q/V can rewrite the above as:
    U = CV2/2 or QV/2

## Slide 12
Capacitance Problem: What if numbers are not so convenient
10.0V across the elements, what is the charge on C1
C1 = 1.0 nF, C2 = 4.0 nF, C3 = 2.0 nF, C4 = 7.0 nF, VAB = 10.0 V
C1
C2
A
B
C4
C3

## Slide 13: Energy Storage in Capacitors
When we charge a capacitor we have stored energy in the capacitor
    U = Q2/2C
Using C=Q/V can rewrite the above as:
    U = CV2/2 or QV/2

## Slide 14: Energy Example
What energy was stored in C1 of previous example ?

## Slide 15: Cap energy multiple choice
Three identical caps are connected to an ideal battery.
Will the system store more energy in the caps are connected in parallel or series?
Parallel
Series

## Slide 16: Capacitors
In real capacitors we place a material between the metal plates because:
  It keeps the metal plates from shorting
  It increases the capacitance
  It increase the “breakdown voltage”

## Slide 17
The charges induced on the surface of the dielectric reduce the electric field.
Dielectric in a capacitor