## Slide 1: HARD AND SOFT WATER

## Slide 2
Hard water
Contains dissolved salts of bicarbonates, sulphates and chlorides of calcium and magnesium.
Hard water does not produce lather with soap solution.
Soft water
Soft water is free from bicarbonates, sulphates and chlorides of calcium and magnisum. It produce lather with soap solution easily.
e.g., distilled water, rain water

## Slide 3
Types of hardness
(i)Temporary hardness
• due to presence of soluble bicarbonates of calcium and magnesium.
• can be removed by simple boiling.
(ii)Permanent hardness
• due to presence of chlorides and sulphates of calcium and magnesium.
• requires treatment of water to remove this type hardness.

## Slide 4
Softening of water
The process of removal of Ca2+ and Mg2+ ions from water is called softening of water.
Removal of temporary hardness:-
Clark’s method or calcium hydroxide method

## Slide 5
Removal of permanent hardness

## Slide 6
Removal of permanent hardness
ii)By using inorganic cation exchanger (permutit method or Zeolite method):
The zeolite can be regenerated by treatment with sodium chloride solution.

## Slide 7
Removal of permanent hardness
(iii) By organic ion exchanger:
Cation exchanger

## Slide 8
Anion exchanger