## Slide 1
METALS

## Slide 2
Introducing metal extraction

## Slide 3: Obtaining metals from ores
First, substances other than the metal compound are removed (concentration).
Next, the metal itself is extracted from its compound (reduction).
Most metals do not occur naturally (native).
They have to be extracted from metal-containing rocks (ores).

## Slide 4: Extraction of metals and energy changes
The more vigorously an element forms compounds the harder it will be to get back that element from its compounds.
For example, magnesium gives out lots of heat when it combines with oxygen.
This means we will have to put lots of energy back to extract magnesium from magnesium oxide and so it will be hard to extract.

## Slide 5: Extraction processes
The Reactivity
Series
potassium
sodium
calcium
magnesium
aluminium
zinc
iron
copper
gold
(carbon)
Increasing reactivity
Metals above carbon must be extracted using electrolysis.
Metals below carbon
can be extracted from the ore by reduction using carbon, coke or charcoal.
Gold and silver often do not need to
be extracted. They occur native.
The reactivity of a metal determines the method of extraction.
lead
silver

## Slide 6: Extraction methods
Here is a list of the symbols of some metals in order of decreasing reactivity-
Li, Ce, Mn, Al, Zn, Cd, Sn, Pb, Cu, Pd
Use this to assign the most likely method of extraction: native (N), carbon(C), electrolysis (E).
Method
(N, C or E)
Symbol
Sn
Cd
Al
Cu
Pd
Ce
Mn
Zn
Li

## Slide 7: Extracting metals
How does the reactivity of a metal affect how easily it can be extracted?

## Slide 8: Extracting gold
Because gold occurs native its extraction is a low-tech affair that simply involves finding it!

## Slide 9: Extracting platinum
Platinum is a rare and expensive metal used in jewellery and also for plating the fuel nozzles in jet engines. It was first discovered by Europeans in 1735 but in South America the primitive pre-Columbian Indians had been using it for centuries.
Approximately where would you place platinum in the reactivity series?
In what form do you think platinum occurs?

## Slide 10
Iron

## Slide 11: Iron
Iron is a moderately reactive metal.
Iron ore (haematite) is plentiful and relatively easily reduced to iron metal by heating with coal (carbon). It is therefore cheap.
It is strong and malleable (non-brittle).
Iron is the most commonly used metal.

## Slide 12: Extracting iron: the blast furnace

## Slide 13: Reactions: reduction of iron ore
carbon + oxygen  carbon dioxide
carbon dioxide + carbon  carbon monoxide
carbon monoxide + iron oxide  iron + carbon dioxide
C (s) + O2 (g)  CO2 (g)
CO2 (g) + C (s)  2CO (g)
3CO (g) + Fe2O3 (s)  2Fe (s) + 3CO2 (g)

## Slide 14: Reactions: removing impurities
calcium carbonate  calcium oxide + carbon dioxide
calcium oxide + silicon dioxide  calcium silicate
CaCO3 (s)  CaO (s) + CO2 (g)
CaO (s) + SiO2 (s)  CaSiO3 (s)
This is called SLAG

## Slide 15: Extraction of iron

## Slide 16
Copper

## Slide 17: Copper
Copper is a metal of low reactivity.
It occasionally occurs native but more often occurs as copper compounds.
Heating copper compounds with carbon gives copper but this is not pure enough to use for electrical work.

## Slide 18: Electrolytic purification
The conductivity of copper is drastically reduced by tiny amounts of impurities.
Because of this, most copper metal is further purified by electrolysis.
In this process, impure copper anodes dissolve.
This dissolved copper is plated onto a cathode leaving behind impurities.

## Slide 19: The cathode
Opposite charges attract.
Positive copper ions (Cu2+) move to the negative cathode.
At the cathode these ions gain electrons and turn into copper atoms.
So, during electrolysis a copper cathode gets thicker.

## Slide 20: The anode
Impure copper is used as the anode of an electrolysis cell.
The battery ‘pulls’ electrons off the copper atoms in the anode.
By losing electrons these atoms become copper ions and so the anode slowly ‘dissolves’ away.
Impurities just sink to the bottom as ‘anode mud’.

## Slide 21: Purification: the whole process

## Slide 22: Purification: the half reactions
Anode (+ve electrode)
Cu (s)  Cu2+ (aq) + 2e-
Cathode (-ve electrode)
Cu2+ (aq) + 2e-  Cu (s)

## Slide 23: Electricity and purifying copper
Copper is purified using electrolysis.
Plan an experiment to investigate factors that might affect the rate of copper production.
Include:
  Any factors that might affect rate.
  The apparatus you would need.
  A statement of how you would control variables.
  The number and range of readings.
  The safety issues you would take into account.

## Slide 24: Purifying copper: answers (1)
Apparatus
Some factors that might affect rate:
  Concentration of solution.
  Distance apart of electrodes
  Electrical potential (volts) or current (amps).
  Duration of electrolysis.
A
3.3g

## Slide 25: Purifying copper: answers (2)
Control of variables
  Basically only change one variable at a time!
Number and range of readings
  Minimum of 8-10 different values
  Repeat readings at least once
  Attempt a range providing a 10-fold change
Safety issues
  Check electrical, toxicity, corrosive, etc.
  Take appropriate measures

## Slide 26
Aluminium

## Slide 27: Aluminium
Aluminium is a reactive metal.
We might expect it to corrode easily but a strong coating of oxide on its surface prevents this in most everyday situations.
It has a low density, which leads to its extensive use in the aerospace industry.
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
O
O
O
O
O
O
O
O
O
Coating of oxygen atoms prevents further attack

## Slide 28: Aluminium ores
Aluminium occurs as the ore bauxite, which is a form of aluminium oxide.
Because aluminium is so reactive, carbon is unable to pull away the oxygen from it.
It is extracted by electrolysis of molten bauxite. Early attempts at this failed because bauxite is so hard to melt.
If cryolite (sodium aluminium fluoride) is added, the bauxite melts more easily. This is an essential step in the extraction process.

## Slide 29: Electrolytic extraction
A bauxite / cryolite mixture is melted in a steel container containing a carbon lining.
Graphite (carbon) anodes
Tank
lined
with
carbon
cathode
Molten electrolyte
bauxite + cryolite
Steel
case
Graphite anodes are inserted into the molten electrolyte ready for electrolysis.

## Slide 30: Production of aluminium
Opposite charges attract.
Positive aluminium ions move towards the negative cathode.
At the cathode these ions gain electrons and turn into aluminium atoms.

## Slide 31: Production of oxygen
Negatively-charged oxide ions move to the anode.
Here they lose two electrons and so turn into neutral oxygen atoms.
These atoms join into pairs to form oxygen gas.

## Slide 32: Production of carbon dioxide
Remember the electrolysis is carried out at high temperature.
Under these conditions quite a lot of the oxygen reacts with the carbon anode.
Carbon dioxide is formed and the anode is rapidly eaten away and frequently has to be replaced.

## Slide 33: Extraction of aluminium: overall
Siphon
Graphite / carbon anodes
Molten aluminium
Molten electrolyte
bauxite + cryolite
Tank
lined
with
carbon
cathode
Molten
aluminium
out
Steel
case
Vented cover

## Slide 34: Extraction of aluminium: half reactions
Anode (+ve electrode)
2O2- (l)  O2 (g) + 4e-
Cathode (-ve electrode)
Al3+ (l) + 3e-  Al (l)
Overall
2Al2O3 (l)  4Al (l) + 3O2 (g)
The anode reacts to form carbon dioxide:
C + O2  CO2

## Slide 35
Summary activities

## Slide 36: Glossary
anode – A positive electrode.
bauxite – The most common type of aluminium ore.
cathode – A negative electrode.
electrolysis – The process of using electricity to cause a chemical reaction.
haematite – A type of iron ore that contains iron (III) oxide.
ore – A naturally-occurring mineral from which a metal can be extracted.
oxidation – A type of reaction involving the loss of electrons.
reduction – A type of reaction involving the gain of electrons.