## Slide 1: MAINS ELECTRICITY

## Slide 2: Specification
Electricity
Mains electricity
understand and identify the hazards of electricity including frayed cables, long cables, damaged plugs, water around sockets, and pushing metal objects into sockets
understand the uses of insulation, double insulation, earthing, fuses and circuit breakers in a range of domestic appliances

## Slide 3: Direct current
Cells and batteries supply electric current which always flows in the same direction.
This is called direct current (d.c.).
Direct current always flows the same way

## Slide 4: Alternating current
An alternating current (a.c.) is one which is constantly changing direction.
Alternating current constantly changes direction.
The lamp works with a.c. and d.c.
~
a.c. power supply

## Slide 5: Mains Electricity
The electricity supplied to our homes is called Mains Electricity.
It is an alternating current supply.
In the UK the current changes direction every 1/100th of a second.
This means it completes a complete cycle of changes every 1/50th of a second.
It therefore has a frequency of 50 cycles per second
or 50 hertz (50 Hz).
How electricity arrives into our homes

## Slide 6: The LIVE and NEUTRAL terminals
UK mains supply is rated at about 230 volts.
This means that it has the same effect as a 230V d.c. battery on devices like a lamp.
One side of the a.c. supply changes constantly between +325V and – 325V.
This terminal is called the LIVE.
Touching this terminal can be fatal!
The other terminal remains at about 0V.
This terminal is called the NEUTRAL.
NEUTRAL
LIVE

## Slide 7: Voltage variation of the LIVE terminal
The voltage of the LIVE terminal varies SINUSOIDALLY between +325V and – 325V taking 1/50th or 0.02 second to complete one complete cycle.

## Slide 8
Choose appropriate words to fill in the gaps below:
_______ current (d.c.) is a current that always flows in ____ direction around a circuit. It is supplied by cells and ________.
Alternating current (a.c.) constantly ________ in direction. The _______ supply to our homes is a.c. In this case the a.c. is supplied at an effective voltage of ______ and a frequency of ______.
An _________ can be used to display and __________ a d.c. or a.c. waveform.
oscilloscope
230V
one
mains
Direct
reverses
50Hz
WORD SELECTION:
batteries
measure

## Slide 9
Choose appropriate words to fill in the gaps below:
_______ current (d.c.) is a current that always flows in ____ direction around a circuit. It is supplied by cells and ________.
Alternating current (a.c.) constantly ________ in direction. The _______ supply to our homes is a.c. In this case the a.c. is supplied at an effective voltage of ______ and a frequency of ______.
An _________ can be used to display and __________ a d.c. or a.c. waveform.
oscilloscope
230V
one
mains
Direct
reverses
50Hz
WORD SELECTION:
batteries
measure
oscilloscope
230V
one
mains
Direct
reverses
50Hz
batteries
measure

## Slide 10: Electrical cable
Electrical cable consists of:
1. A LIVE wire
with BROWN insulation
2. A NEUTRAL wire
with BLUE insulation
and except with some devices with plastic cases
3. An EARTH wire
with YELLOW-GREEN striped insulation.
These are all surrounded by an outer layer made of rubber or flexible plastic.

## Slide 11: The EARTH wire
This is a safety feature.
The earth wire is connected to the metal casing of a device.
The other end of this wire is connected to a metal rod or pipe that goes into the ground below a building.
Appliances that have plastic cases, for example hairdryers, do not need the earth wire connection.
EARTH

## Slide 12: The three pin plug

## Slide 13: Materials used in plugs, sockets and wires
BRASS – Hard rigid metal and electrical conductor
– used for plug pins and socket terminals
COPPER – Flexible electrical conductor
– used for the wires
PLASTIC – Hard rigid electrical insulator
– used to make the plug and socket
RUBBER – Soft flexible electrical insulator
– used for wire insulation

## Slide 14: Label this diagram
2.
1.
3.
5.
4.

## Slide 15: Label this diagram
2.
1.
3.
5.
4.

## Slide 16: Label this diagram
fuse
live
neutral
earth
2.
1.
3.
5.
4.
cable grip

## Slide 17: What is wrong with this plug’s wiring?
Note: The appliance connected with this plug would probably still work but it would be very dangerous to use!
Earth wire not connected
Wire untidily connected – some bare strands of wire showing
Live and neutral wires swopped over
Cable grip not gripping the outer plastic insulator

## Slide 18
Choose appropriate words to fill in the gaps below:
Most electrical cables contain _______ separately insulated wires. ______-core cables are only used with appliances that have _______ casings.
The live wire has _______ insulation, the neutral has ______and the _______ has striped yellow-green.
In a 3-pin plug the live is connected on the ______ next to the fuse. The neutral is on the ______and the earth is connected at the top.
left
right
brown
blue
three
two
plastic
WORD SELECTION:
earth

## Slide 19
Choose appropriate words to fill in the gaps below:
Most electrical cables contain _______ separately insulated wires. ______-core cables are only used with appliances that have _______ casings.
The live wire has _______ insulation, the neutral has ______and the _______ has striped yellow-green.
In a 3-pin plug the live is connected on the ______ next to the fuse. The neutral is on the ______and the earth is connected at the top.
left
right
brown
blue
three
two
plastic
WORD SELECTION:
earth
left
right
brown
blue
three
two
plastic
earth

## Slide 20: The Dangers of Mains Electricity
The two main dangers of mains electricity are:
1. FIRE
This can be caused by too high a current flowing along cables or through appliances.
A fuse or circuit breaker is used to limit the current to a safe level.
2. ELECTROCUTION
This can occur when contact is made with the LIVE wire. Death can occur if a current above about 100mA (0.1A) flows through the body.
The EARTH wire in combination with a fuse or circuit breaker can prevent electrocution.

## Slide 21: Fuses
Internal fuse from an appliance
A fuse is a length of wire designed to melt and so breaking a circuit when the current passing through it goes above a certain level.
Fuse wires
3A, 5A and 13A fuses used in 3-pin plugs
Cartridge used with fuse wire

## Slide 22
The thicker the fuse wire the greater is the current required to cause it to melt (or fuse).
Fuses are only supplied with a limited number of ratings.
Modern circuit symbol for a fuse

## Slide 23: Circuit Breakers
A circuit breaker is an electromagnetic device that breaks a circuit when the current goes above a certain value.
RCD (Residual Current Device) circuit breaker used with an individual appliance
Circuit breakers in a consumer unit

## Slide 24: A simple circuit breaker
A
B
Current normally flows between terminals A and B through the contact and the electromagnet.
When the current in a circuit increases, the strength of the electromagnet will also increase. This will pull the soft iron armature towards the electromagnet.
As a result, spring 1 pulls apart the contact and disconnecting the circuit immediately, and stopping current flow.
The reset button can be pushed to bring the contact back to its original position to reconnect the circuit
1
2

## Slide 25: Comparison of fuses and circuit breakers
Both can prevent fire by limiting the current flowing through a cable or appliance.
Fuses are simple and are cheap to replace.
Circuit breakers act more quickly than fuses and can be reset.
Comparison of fuses and circuit breakers

## Slide 26: The action of the EARTH wire
Appliances with metal cases such as a tumble dryer are usually earthed by having the EARTH wire connected to their metal case.
Normally current flows to and fro between the LIVE and NEUTRAL wires through the heater of the dryer.
The metal case is at zero volts and is safe to touch.
fuse
earth wire connected to metal case
insulation
heater
metal case of tumble dryer
L
N
E

## Slide 27: The action of the EARTH wire
If the LIVE wire became loose inside the dryer it might touch the metal case.
The metal case would now be dangerous to touch and could give a fatal electric shock.
However, the EARTH wire provides a low resistance path to the ground.
fuse
earth wire connected to metal case
insulation
heater
metal case of tumble dryer
L
N
E

## Slide 28: The action of the EARTH wire
A large current now flows through the fuse and causes it to melt.
The dryer’s metal casing is now isolated from the LIVE connection and is safe to touch.
fuse
earth wire connected to metal case
insulation
heater
metal case of tumble dryer
L
N
E

## Slide 29: Double insulation
Many electrical appliances have casings made from an insulator such as plastic rather than metal. The electrical parts of the device cannot therefore be touched by the user.
The appliance is said to have double insulation. Such appliances will only have two-wire cables as they do not need the EARTH wire.
Plug wiring for a device with double insulation
Plastic cased food mixer will have double insulation
Symbol found on devices having double insulation

## Slide 30
How many dangerous practices can you spot in the picture below?

## Slide 31
Choose appropriate words to fill in the gaps below:
Two dangers of mains electricity are ____ and electrocution.
Fires are caused when too high a ________ is allowed to flow along cables. Current can be limited by placing a ______ or circuit breaker in the _____ wire.
The _______ wire is used to prevent the metal casing of an appliance from becoming live should a wiring fault occur. A _______ current flowing down the earth wire will cause the fuse or circuit breaker to _________ the live connection.
isolate
large
fuse
fire
current
earth
WORD SELECTION:
live

## Slide 32
Choose appropriate words to fill in the gaps below:
Two dangers of mains electricity are ____ and electrocution.
Fires are caused when too high a ________ is allowed to flow along cables. Current can be limited by placing a ______ or circuit breaker in the _____ wire.
The _______ wire is used to prevent the metal casing of an appliance from becoming live should a wiring fault occur. A _______ current flowing down the earth wire will cause the fuse or circuit breaker to _________ the live connection.
isolate
large
fuse
fire
current
earth
WORD SELECTION:
live
isolate
large
fuse
fire
current
earth
live

## Slide 33: Complete:
Device and power (W) | Normal current (A) | Fuse choice from: 3A, 5A or 13A
Computer; 300W |  | 
Microwave; 900W |  | 
Charger; 10W |  | 
Heater; 2kW |  | 
Maximum power? | 13A | 
Answers
1.3 A
All of the devices below are 230V mains appliances.
0.04A
8.7A
3.9 A
2990W

## Slide 34: Complete:
Device and power (W) | Normal current (A) | Fuse choice from: 3A, 5A or 13A
Computer; 300W |  | 
Microwave; 900W |  | 
Charger; 10W |  | 
Heater; 2kW |  | 
Maximum power? | 13A | 13A
Answers
3A
5A
1.3 A
3A
All of the devices below are 230V mains appliances.
0.04A
8.7A
3.9 A
13A
2990W