## Slide 1
LATITUDES AND LONGITUDES

## Slide 2: Angular Distance – Latitude (1/11)
North Pole
South Pole
θ
φ
Latitude is the
angle of a point
above
or
below
the equator

## Slide 3: Latitude (2/11)
North Pole
South Pole
Small circles
parallel to the equator
are called
Parallels of Latitude.
They are the angle
between the
small circle and
The equator.
50o
Latitude = 50oN

## Slide 4: Latitude (3/11)
North Pole
South Pole
30o
Latitude = 30oS

## Slide 5: Angular Distance – Opposite Sides (4/11)
North Pole
South Pole
The angular distance
for angles
on opposite sides
of the equator
can be found by
adding the angles
50o
50oN + 30oS =
30o
80o

## Slide 6: Angular Distance – Same Side (5/11)
North Pole
South Pole
The angular distance
for angles
on the same side
of the equator
can be found by
subtracting
the angles.
50o
50oN - 30oS =
30o
20o

## Slide 7: Distance - Nautical Miles – Opposite Sides (6/11)
North Pole
South Pole
50o
30o
1o = 60 Nautical Mile (M)
50oN + 30oS = 80o
80o = 80 x 60M
[1M ≈ 1.853 km]
4800M ≈ 4800 x 1.853
= 8894.4
= 4800 M
= 8900 km

## Slide 8: Distance - Nautical Miles – Same Side (7/11)
North Pole
South Pole
50o
30o
1o = 60 Nautical Mile (M)
50oN - 30oS = 20o
20o = 20 x 60M
[1M ≈ 1.853 km]
1200M ≈ 1200 x 1.853
= 2223.6
= 1200 M
= 2200 km

## Slide 9: Distance - Great Circle (8/11)
North Pole
South Pole
Earth Radius ≈ 6400 km
70o
D = x 2 r
≈ x 2 x 6400
θ
360
70
360
≈ 78190.075049
≈ 78,200 km

## Slide 10: Distance – Great Circle (9/11)
North Pole
South Pole
30o
Earth Radius ≈ 6400 km
D = x 2 r
≈ x 2 x 6400
θ
360
30
360
≈ 3,351.032164
≈ 3,400 km

## Slide 11: Distance - Speed (10/11)
North Pole
South Pole
1 knot = 1 M/hr
70o
D = 70 x 60 M
An airplane travels 70o
along a great circle in
10 hours.
What is its speed?
= 4200 M
Speed = 4200 ÷ 10
= 420 M/hr
= 420 knots

## Slide 12: Distance – Great Circle (11/11)
North Pole
South Pole
5o
1 knot = 1 M/hr
D = 5 x 60 M
An ship travels 5o
along a great circle in
5 hours.
What is its speed?
= 300 M
Speed = 300 ÷ 5
= 60 M/hr
= 60 knots